##### STUDIO THEATRE Technical information

Our Studio theatre is a very lovely space, but we want to be as clear as possible about our limitations.

Attached are a few photos of the space including back wall, and the tech spec.

If the wall of serge flats (see photo below) is needed, it’s worth noting the pitched roof.

Limited Dressing room facilities (At least one small proper dressing room) plus use of comfortable green room.

Get-in next to stage door via 2 x 1.2m wide sets of fire exit doors up one flight of straight stairs. Also through 2 x single doors via small passenger lift.

# LIGHTING EQUIPMENT

## Control

1           ETC                    Colorsource 20                Programmable Memory Desk       DMX

### Dimmers

3           Zero 88                   Betapack                  Double 15amp Dimmer Packs

1 	Strand			DIM 1 			Single 15amp pack, for Houselights

#### Lanterns

5    Rank Strand	Prelude 28/40	27-40deg profiles	   650watt

5	Strand   	Prelude PC  			   500w c/w barn doors

3 Selecon	Fresnel				650w c/w barn doors

6	Strand	Pattern 743     45 deg 	   	  1kw  c/w barn doors

3      small floods as houselights

(Other equipment pending stock availability from main house)

### Rigging

Limited hanging points for scenery – Please check.

Assorted Barrel and Fixings

3 x  Socapex Multicore and assorted cables

### Electricity Supply

3 Phase supply fused at 20amps per phase, terminated in 63 amp sockets.

### SOUND EQUIPMENT

1   Soundcraft     Spirit powerstation     8 + 2 stereo  Channel  Mixing Desk

Playback  MD & CD players (pending stock availability from main house)

2 EV SX200 speakers

###### Equipment Availability

###### It is at times necessary to remove items of stock for maintenance or health and safety

###### reasons, Therefore the   entire stock listed above may not be available. Visiting companies

###### are advised to complete and return  all plans, colour calls, etc. 14 days in advance of your

###### get-in to ensure that the required equipment and  consumables can be made available

Stage Dimensions

Oblong room - 10.5m x 8.0m. Windows at Stage end which can be blacked out.

Flat Floor End stage with single raked bank of seats – up to 50

Front row on floor, rest on rostra

Stage  floor  - 8.0m wide , 5.0m deep to front row.

Pitched roof slopes from 2.1m to 4.3m

2.5- 3.5m clearance over most of playing area

2 exits, both available for performers, both in view of audience

Can create back wall or wings using 3 of 8’ x 4’ black serge flats as a “backstage” for performers to be preset

Any queries, please contact	 Adam Gent 	 Production Manager – 0161 785 7027

adamgent@coliseum.org.uk

# Text boxes

Stage area

Single door to dressing rooms or exit

Front Row seats

Snd &LX

Control

Seating Rostra